MC Template Guide

Procedure

- log in: ssh –XY user@lxplus.cern.ch

- go to the production directory to have a look at the current job repositories:

cd /afs/cern.ch/ams/Offline/AMSDataDir/DataManagement/DataSets

- create your MC folder: mkdir name.BXYZ (for example antiprotons.g4.v5.B550) somewhere in /f2users (for example in /afs/ams.cern.ch/scratch/user/)

- cd name.BXYZ

- create two void tag files:

touch version=v5.00

touch g4=true

- and the one for the repository: touch build=.BXYZ     (note the dot)

- put your MC  job template name.pl1.energyrange.job   in this folder and copy your name.BXYZ folder into  /Templates2Add :

cp -r /afs/ams.cern.ch/scratch/user/name.BXYZ /afs/cern.ch/ams/Offline/AMSDataDir/DataManagement/Templates2Add/

- Tell Choutko where the templates are; go to production page and check the jobs are available for production. First you have to do

$ ssh -v -L 2080:pcamss0.cern.ch:80  myname@lxplus.cern.ch        (or cern.ch:23)

and then set a localhost:2080 proxy SOCKSv5 on your browser

- Then you can go to

http://pcamss0.cern.ch/mm.html   Production Status; or control symbolic links in /afs/cern.ch/ams/Offline/DataSetsDir/MC/AMS02/2011B/

All MC rootfiles should be transferred in 48 hours to CNAF  /storage/gpfs_ams/ams/Rec/MC/2011B/ directory.

A Template Explained: how to write a MC job

Directory: /afs/cern.ch/ams/Offline/AMSDataDirRW/DataManagement/DataSets/antiprotons.g4.v5.B512

File Name:  antipr.pl1.0510.job  (name.pl1.energyrange.job)

#generate antiprotons  g4  from 3.9m cube top plane (log spectrum) 0.5-10 GeV  v5

OPENCLOSE=3                              //usually 3 (or 0):  0/1/2/3 = cern/notcern/all/ spec cite

ROOTNTUPLE=                             //leave it blank – it connects to IOPA

PART=15	            //particle id -  1:photon,  2:positron,  3:electron,  5:mu+,  14:proton,   15:antiproton,  47:He(4),  49:He3,  64:Be9,   67:Ca(12), 114:Be10 …etc…

PMIN=0.5                                    // minimum momentum in GeV

PMAX=10.		           //maximum momentum in GeV (<8000)

TIMBEG=20102011	          // GMT time begin (Fri, 21 Aug 1970 15:53:31)

TIMEND=31122019	 //GMT time end (Sun, 27 Dec 1970 05:00:19) – past history range for MC rootfiles – don’t touch

TOTALEVENTS=10000000       //from 10 millions to 10 billions  (Trigger events)

CPUPEREVENTPERGHZ=0.16    //cpu per event per GHz, order of magnitude: 0.005 to 10,

// cern openclose=3  2.2 GHz (usually 0.15÷0.17)

// It’s important to use three momentum ranges, with correct CPU and Trigger values, for example:

0.5-10 GeV          ----> CPU=0.007   trig=5*10^7        2 days

10-200 GeV          ----> CPU=0.07    trig=3*10^7      11 days

200-4000 GeV     ----> CPU=0.2      trig=10^7	         11 days

following the formula to compute the time for MC rootfile production:   days=CPU*Trig/(2.2*60*60*24)=CPU*Trig/190080

LIST

Constant parameters

KINE $PART

LOSS 1

HADR 1

MULS 1

CUTS 1=0.0005 2=0.0005 3=0.001 4=0.001 5=0.001

TRIG $TRIG

DEBUG -1 10 1000

MCGEN  12=-0.7  13=$PMIN 14=$PMAX 15=1 19=$RUN  20=5 21=0 34=0     //typical configuration

//	"MC particle generation" - Parameters for the particle production

12=$COST ---> max cos(theta) angle

13=$PMIN ---> it takes the previous value

14=$PMAX ---> it takes the previous value

15=      ---> fix the cube surface for particle:

0-->no surfaces fixed

1--> fix the first(top), 2-->fix the second(bottom)

19=$RUN  ---> run number

20= 	 ---> spectrum number

0  Cosmic spectrum

1  UnderCutoff spectrum

2  Sea Level Muons Spectrum

3  Mev Range Electron Spectrum

4  Uniform in momentum Spectrum

5  Uninform in log(momentum) Spectrum

21=  	----> Earth magnetic field modulation

on (1) or off (0)

34= 	----> special acceptance cut

- Default(None)

1      focus on ecal

2     focus on outer trd hc

3      focus on solar panel/ams (AMS02BIG setup required)

10+  additional tracker plane on the ecal level

IOPA $ROOTNTUPLE'$NtupleDir/pl1/$PART'                    //rootfile with the output name and links (pl1 shall be    useful in future)

43=101 45='TriggerLVL1 ' 126=50000 168=120000000   //Other parameters: typical good configuration

//

43=	----> Flag to write objects into the ntuple: 100+X (X=1 -->All)

101 means: write events with errors for All ntuples

1=All;

0=Only "used" objects;

2="Used" + tracker hits consistent with TOF

45=    ----> trigger type

126=   ---->  max entries for ntuples (default 100000)

168=   ----> max ntuplefilesize in Kbytes (default 100000000)

RNDM $RNDM1 $RNDM2            // initial random seed1 seed2

C      Simul Debug    CpuLim  Read Write Jobname        //comment

AMSJOB 1=10000   2=0      3=$CPULIM   4=0  5=0         //typical good configuration

// Some general features for the job

1=   ----> job type

10000 corresponds to Production

2=   ----> Debug 0 - Off   ; 1 - On

3=   ----> CpuLimit in native sec per event

4=   ----> Read  0 - Off; 1 – setup; 10 – Mceventg; 100 -mc banks; 1000 - Rec banks

5=   ----> Write (same options)

C Special HP-UX					//comment

TIME 3=10000000                 			// time for program execution – standard value

TERM 1234567890				//usual datacard check: Ok if == 1234567890 stop otherwise

L3REC 11=0					//LVL3 Trigger

11= ---> Min value of lvl3 trigger to accept

C MAGS 1=1 					// magnet Simulation/status (-1/0/1->warm/cold_OFF/cold_ON)

C Skip ROOT files DAQC 127=1	                            //comment

DAQC 1=610 42='$NtupleDir/' 			// DAQ Control, don’t touch

END

!

Other commands (standard settings)

TRFIT  71=1		// Tracker pattern recognition

71 = ----> LowMargin(Default 0)

use/not use any 5 planes patterns for track reconstruction (>=1 always use)

TRDFI  7=2 8=0		// TRD Fit & other

7=  ----> FitMethod

old (0) or new (1) or both (2) method

8=  ----> SaveHistos

save single tube amplitude spectra (1) or not (0)

//AMS Global Reconstruction:

BETAFIT  20=2		// fit di beta

20=  ----> Old or New method

Two digit MN

M==0 Master New, M==1 Master old

N==0 -> N beta ;

N==1 Beta new;

N==2 Beta old ;

N==3 Beta Old & New;

TKGEOM  807=11            // for TRK disalignment studies